## Slide 1: Robotic Football
Dan Ridzik, Aidan Shaughnessy, Peter Ryan, Matt Domenech

## Slide 2: Introduction
Robotic football, what is it?
How does it work?
Why complete passes?

## Slide 3: Problem Description
Passes are near impossible
  Why? No way to know QB-WR distance
Current System: Pixicam
  Pros: Gets very accurate reading laterally
  Cons: Don’t know vertical distance

## Slide 4: Proposed Solution
Decawave indoor positioning chip
Use RF Flight times to get positioning data
Beacons triangulate location

## Slide 5: Proposed Solution
Beacons continuously send and receive RF signals from the WR’s and QB
Relay this back only to the QB
QB continuously calculates distance between itself and receivers
  Adjusts rotor speed of throwing mechanism accordingly

## Slide 6: Completing A Pass
User will select a receiver to throw to
Override signal is sent to the QB
  Sets the RPM of throwing mechanism using only the distance of the selected receiver
  Not the closest receiver
The pixicam system then locates and locks onto the receiver
  If interference occurs, data can then be obtained through the RF beacon system

## Slide 7: Demonstrated Features
Location of the QB and WR’s
  six RF beacon emitters and receivers
  The QB and three WR’s are being tracked in real time
Limit weight of technology
  GPS technology cannot exceed the size of the robots
  Don’t want to weigh the robots down
  Determine what percentage of the robot weight is being contributed by our technology.

## Slide 8: Demonstrated Features
Build quality: must be able to absorb significant impact
    Robots collide at high speeds, often causing damage
Quick access to modules in case of “injury”
    Should the system break, the system must be able to be fixed
Adjusting Wheel Speed of QB’s “Throwing Motion”
    System must connect directly to the QB’s mainframe
Automatically adjust RPM of the throwing mechanism
    Must continually adjust with the play

## Slide 9: Available Technologies
DecaWave DW1000 chip for indoor location via radio frequency
  Placed in our sideline beacons and robots
We will be using bluetooth technology (xbee) to communicate between controllers and robots
  How RFC currently communicates between the controller and robots
Make our own circuit boards for each beacon/robot
Use our own power supply (Lithium Ion battery)
  Avoid killing entire robot in case of malfunction.

## Slide 10: Available Technologies

## Slide 11: Engineering Content
Design and build 4 to 6 beacons from scratch.
  Purpose: to track location and transmit data to the QB.
Design and build 3 modules for WRs and 1 module for the QB.
  Purpose: to differentiate trackable robots from non-trackable robots.
Test accuracy of the system in a game-speed environment.

## Slide 12: Conclusions
One pressing concern: RFC informed the team that the beacon system may not be allowed at official tournaments.
If this is the case, a restricted version of the solution may be implemented
  Instead of beacons, RF signals will be sent and received by the QB robot.
This will hinder the ultimate future goal, but this system still greatly improves upon the current pixicam system

## Slide 13: Conclusions
Project contains a combination of software and hardware components
  More research must be completed prior to construction
Project must be completed in time for the RFC to use in March at the tournament

## Slide 14
http://dailydomer.nd.edu/assets/72433/original/4.20.12_robot_football_2.jpg
https://www.decawave.com/sites/default/files/styles/front_page_slider_image/public/dw1000_new_0.png?itok=EOOfOriZ
https://www3.nd.edu/~rfc/pages/2016-2017/gallery/pics/003.jpg